## Slide 1
Mass Storage Structure

## Slide 2: Overview of Mass Storage Structure
Magnetic disks provide bulk of secondary storage of modern computers
  Drives rotate at 60 to 250 times per second
  Transfer rate is rate at which data flow between drive and computer
  Positioning time or random-access time or seek time is time to move disk arm to desired cylinder
  rotational latency
  Head crash results from disk head making contact with the disk surface

## Slide 3: Cont..
Drive attached to computer via I/O bus
  Busses vary, including EIDE, ATA, SATA, USB, Fibre Channel, SCSI, SAS, Firewire
  Host controller in computer uses bus to talk to disk controller built into drive or storage array

## Slide 4
Moving-head Disk Mechanism

## Slide 5: Disk Structure
Disk drives are addressed as large 1-dimensional arrays of logical blocks
Where the logical block is the smallest unit of transfer
  Low-level formatting creates logical blocks on physical media
The 1-dimensional array of logical blocks is mapped into the sectors of the disk sequentially
  Sector 0 is the first sector of the first track on the outermost cylinder
  Logical to physical address should be easy
    Except for bad sectors
    Non-constant of sectors per track via constant angular velocity

## Slide 6: Disk Management
Low-level formatting, or physical formatting
  Each sector can hold header information, plus data, plus error correction code (ECC)
  Usually 512 bytes of data but can be selectable
To use a disk to hold files, the operating system still needs to record its own data structures on the disk
  Partition
  Logical formatting or “making a file system”

## Slide 7: Cont..
  To increase efficiency most file systems group blocks into clusters
    Disk I/O done in blocks
    File I/O done in clusters
Boot block initializes system
  The bootstrap is stored in ROM
  Bootstrap loader program stored in boot blocks of boot partition
Methods such as sector sparing used to handle bad blocks

## Slide 8
Booting from a Disk in Windows

## Slide 9: Disk Scheduling
The operating system is responsible for using hardware efficiently
Minimize seek time
Seek time  seek distance
Disk bandwidth
Disk Access Time = Seek Time + Rotational Latency + Transfer Time
Total Seek Time = Total head Movement * Seek Time

## Slide 10: Cont..
There are many sources of disk I/O request
  OS
  System processes
  Users processes
Several algorithms exist to schedule the servicing of disk I/O requests
We illustrate scheduling algorithms with a request queue (0-199)
98, 183, 37, 122, 14, 124, 65, 67

## Slide 11
FCFS
Illustration shows total head movement of 640 cylinders

## Slide 12: SSTF
Shortest Seek Time First selects the request with the minimum seek time from the current head position
SSTF scheduling is a form of SJF scheduling; may cause starvation of some requests
Illustration shows total head movement of 236 cylinders

## Slide 13
SSTF (Cont..)

## Slide 14: SCAN
The disk arm starts at one end of the disk, and moves toward the other end, servicing requests until it gets to the other end of the disk, where the head movement is reversed and servicing continues
SCAN algorithm Sometimes called the elevator algorithm
But note that if requests are uniformly dense, largest density at other end of disk and those wait the longest

## Slide 15
SCAN (Cont.)
= (199-50) + (199-16) = 332

## Slide 16: C-SCAN
Provides a more uniform wait time than SCAN
The head moves from one end of the disk to the other, servicing requests as it goes
  When it reaches the other end, however, it immediately returns to the beginning of the disk, without servicing any requests on the return trip
Treats the cylinders as a circular list that wraps around from the last cylinder to the first one

## Slide 17
C-SCAN (Cont.)
=(199-50) + (199-0) + (43-0) = 391

## Slide 18: C-LOOK
LOOK a version of SCAN, C-LOOK a version of C-SCAN
Arm only goes as far as the last request in each direction, then reverses direction immediately, without first going all the way to the end of the disk

## Slide 19
C-LOOK (Cont.)
C-LOOK (Cont.)

## Slide 20: Swap-Space Management
Swap-space — Virtual memory uses disk space as an extension of main memory
Swap-space can be carved out of the normal file system, or, more commonly, it can be in a separate disk partition (raw)
Swap-space management
  4.3BSD allocates swap space when process starts; holds text segment (the program) and data segment
  Kernel uses swap maps to track swap-space use
  Solaris 2 allocates swap space only when a dirty page is forced out of physical memory, not when the virtual memory page is first created

## Slide 21: Data Structures for Swapping on Linux Systems